## Slide 1
SECTION 9 · WHY THIS MATTERS FOR YOU
Lesson 1 — It is a throughput machine
1
THE HISTORY THAT EXPLAINS IT
Gaming economics built it: millions of $300 cards, not thousands of $100k workstations — the volume flywheel from Section 2.
A frame is millions of independent pixels; latency on any one of them is irrelevant. The silicon inherited that: thousands of small, slow, simple cores.
Nothing about CUDA changed the economics — compute rides on hardware shaped by games.
THE PRACTICE IT DEMANDS
The first question of any port is not “how fast is the GPU?” but “is there enough parallel work to be worth the trip?”
Small or serial work often loses, sometimes by orders of magnitude. One fast core beats a thousand slow ones on a serial problem.
Throughput-over-latency is not a setting. It is the machine.
The machine is a consequence of who paid for it. Program the economics, not the brochure.
Notes: Lesson slides all follow: history left, practice right. This one is the foundation - everything else assumes the audience accepts throughput-over-latency as baked in.

## Slide 2
SECTION 9 · WHY THIS MATTERS FOR YOU
Lesson 2 — The programming model is the hardware
2
THE HISTORY THAT EXPLAINS IT
Section 1’s bargain: every pixel decided independently. The model was always there — one function over many independent elements.
Section 4’s hacks proved it: floats disguised as pixel colors, matrices as textures — general compute forced through a graphics-shaped hole.
Brook (2004) named it — streams and kernels — and CUDA (2006) made it the native tongue.
THE PRACTICE IT DEMANDS
Data-parallel code ports almost by transcription: one kernel, many elements, no cross-talk.
Deeply serial code must be rethought, not translated. If element i needs element i−1, you are fighting the machine’s founding assumption.
Ask of every loop: are the iterations strangers to each other?
N
MATRIX ADDITION AS PIXELS · §4 NOTE
CUDA did not invent the model — it stopped requiring the disguise. The hardware’s shape was the model all along.
Notes: The matrixAddition rabbit hole (floats packed into RGBA texels) is the visceral proof that the model predates the API. Open it if anyone doubts the 'disguise' framing.

## Slide 3
SECTION 9 · WHY THIS MATTERS FOR YOU
Lesson 3 — Call a library, not a kernel
3
THE HISTORY THAT EXPLAINS IT
Section 5’s bet: the integrated proprietary stack — CUDA plus its libraries — beat the open alternative that shipped as a spec.
cuBLAS, cuFFT, cuSOLVER, cuDNN: vendor kernels tuned per architecture, by the people who designed the silicon.
When tensor cores arrived in 2017, updated libraries could expose them with little or no application-code change.
THE PRACTICE IT DEMANDS
On common operations, hand-written kernels often lose to vendor libraries — and may age worse across hardware generations.
Write to the operation, not the device: say “multiply these matrices,” let the library choose the silicon.
Your own kernels are for the glue between library calls — not the linear algebra inside them.
N
THE RUNWAY AND THE PLANE · §7 NOTE
The library is the contract that outlives the hardware. It is also the usual door to the tensor cores.
Notes: cudaLuck callback: the libraries were the runway. AlexNet was the plane. Deliberate skill was recognizing the landing within months - cuDNN 2014, DGX, the pivot.

## Slide 4
SECTION 9 · WHY THIS MATTERS FOR YOU
Lesson 4 — Moving data is the hidden cost
4
THE HISTORY THAT EXPLAINS IT
The GPU is a coprocessor across a bus — Section 6’s HPC skeptics said exactly this, and they were right; it just was not fatal.
Tianhe-1A and Titan won by keeping data resident on the device, not by shuttling it per operation.
The exception proves the rule: matmul’s n³-on-n² is why it can be frozen at all (Slide 4).
THE PRACTICE IT DEMANDS
Arithmetic per byte moved must pay for the move. Count it before you port — this is the roofline question.
Keep data resident: chain operations on the device; the worst pattern is transfer–compute–transfer per step.
A slow GPU port may be a transfer problem wearing a compute costume.
The bus never got fast enough to stop mattering. Every fast GPU program is, first, a data-residency design.
Notes: This is the bridge to the Roofline Simulator companion - the measurement discipline lives there. The HPC-objection framing gives the skeptics their due (expertResistance pattern).

## Slide 5
SECTION 9 · WHY THIS MATTERS FOR YOU
Lesson 5 — Small costs; priced precision
5
LAUNCH OVERHEAD · THE HISTORY
Each kernel launch costs microseconds of host round-trip — invisible once, ruinous a million times.
The fixes are structural: batch the work, fuse the kernels, capture-and-replay the whole graph (CUDA Graphs).
PRECISION · THE PRICE LIST
FP64 on consumer cards: 1:8 → 1:24 → 1:32 → 1:64 of FP32, generation by generation — a business decision, not physics (Section 6).
Tensor cores dial the other way: FP16 → INT8 → INT4 — precision engineered as a spectrum, priced by the workload.
Choose precision like you choose an algorithm: deliberately, and check what your card actually provides.
The FP64 penalty in the offload guide is a price list, not a law of nature. Read the price list before you design.
Notes: Two independent small-print lessons on one slide. The 1:8-to-1:64 sequence is verified in the document's claims ledger (#21); the EULA moment (2017, legal limit replacing technical) is worth telling aloud.

## Slide 6
SECTION 9 · WHY THIS MATTERS FOR YOU
Lesson 5, continued — precision in practice
CHECK THE FP64 LINE FIRST
datacenter ≈ 1:2 · consumer 1:8 → 1:64
GPUs are not one machine. Many datacenter parts run double precision near half the FP32 rate — engineering-grade FP64 at high speed. Consumer cards of the same generation may be limited to 1:32–1:64, deliberately. If your work leans on FP64 — structural dynamics, covariance solves, anywhere conditioning bites — the card class is the first architectural decision you make. One line of the spec sheet decides the design.
16-BIT IS A MEMORY STORY, NOT AN ARITHMETIC ONE
Many important kernels are memory-bound (Lesson 4). Halve the width and twice as many values arrive per fetch; the working set halves; every cache line carries double. A bandwidth-limited kernel speeds up ~2× in FP16 with no tensor cores and no new ALUs — the arithmetic was never the bottleneck. Precision is a data-movement dial first, and a compute dial second.
THE DECISION PROCEDURE
Locate the kernel on the roofline first: memory-bound or compute-bound? (The companion lab exists for exactly this question.)
Memory-bound → cut bytes: consider lower precision, then recover accuracy where appropriate through iterative refinement.
Compute-bound matmul → the tensor-core menu sets your formats. FP64-dominated → buy the datacenter part, or do not offload.
Precision is priced twice: once in silicon — the FP64 market segment — and once in bytes — the bandwidth bill. Read both price lists before you design.
Notes: The two additions: (1) FP64 is not gone from GPUs - datacenter silicon runs it at 1:2; only the consumer segment is capped (ratios per the document's verified claim #21) - so 'check the spec line' is a real design step, not paranoia. (2) The deep reason low precision wins on most kernels is bandwidth, not FLOPs: bytes halve, effective bandwidth doubles, and that pays even on hardware with no tensor cores at all. The QUDA example (8-bit block floats inside double outer solves, verified this session from the QUDA project page) shows iterative refinement making aggressive precision safe in production physics.