## Slide 1
GPU Offload Triage Procedure
Evaluating OpenMP code with independent iterations,
expensive parallel build phases, and small-matrix solvers
for GPU migration.
Shore Western Manufacturing

## Slide 2
THE PATTERN
OpenMP + Expensive Build + Small Solver
Outer loop dispatched through #pragma omp parallel for. Iterations are independent — no state carried from iteration k to k+1.
Each iteration: an expensive, fully data-parallel build phase constructs a matrix. This dominates runtime.
Then a barrier or lock ensures the build is complete.
Then a small-matrix Cholesky / triangular solve / dense linear algebra phase runs on the built matrix.
The solver is small — below the single-problem GPU crossover. One cuSOLVER call at this N is slower than MKL.
The per-iteration triage says "too small for GPU." That conclusion is wrong if the iterations are independent.

## Slide 3
STEP 0
Read the Code — Identify the Outer Loop
What is the iteration structure? OpenMP parallel for on the outer loop — iterations claimed independent.
Is there iteration-to-iteration coupling? Verify: does iteration k+1 read results written by iteration k? If not, iterations are truly independent.
Do any called functions take a mutex? Classify each lock — most are Category 5 phase gates between the parallel build and the serial solver.
The diagnostic: remove every lock, run single-threaded. Same answer? Then the locks are thread-safety infrastructure, not algorithmic dependence.
The key finding at Step 0: iterations are independent. This opens the batching path that the per-iteration analysis misses.

## Slide 4
STEP 0d
Classify Each Lock
Cat 1 — Accumulation
Hidden reduction. Replace with omp reduction or GPU atomic. Lock disappears.
Cat 4 — Infrastructure
Allocator, handle pool, logging. Strip from analysis. Not algorithmic.
Cat 5 — Phase Gate
Parallel build → barrier → solver. Free on GPU: stream ordering = barrier. This is your pattern.
Cat 2/3 — True Dependency
Shared mutable state or ordering constraint. If present, iterations are NOT independent. Resolve before proceeding.
For this pattern, the lock between build and solver is Category 5 — a phase gate that costs zero on GPU.

## Slide 5
STEP 1
Profile One Iteration, Single-Threaded
Strip the outer OpenMP. Remove every mutex. Run the bare iteration body once, single-threaded, under a profiler. That trace is the GPU migration unit.
Measure the cost split: how much time in the build phase vs the solver phase?
The build phase is data-parallel — perfect GPU kernel candidate regardless of matrix size.
The solver phase is small-N dense linear algebra — per-iteration, cuSOLVER is slower than MKL.
This per-iteration analysis gives the correct phase classification but the wrong offload conclusion. Proceed to Step 6.

## Slide 6
STEP 2
The Solver Loop Should Not Exist
Does the solver implement a named operation? Cholesky, triangular solve, LU, QR, SVD?
If yes: replace the hand-written loop with a vendor library call. On CPU, MKL dpotrf + dpotrs. On GPU, cuSOLVER or cusolverDnDpotrfBatched.
The comparison that matters: optimized CPU library vs optimized GPU library — not hand-written loop vs GPU.
At small N, a single cuSOLVER call is slower than MKL. But that is the per-iteration comparison. With independent iterations, the relevant comparison is batched cuSOLVER vs threaded MKL.
The profiler says "not offloadable" because the source loop is dependency-bound. The engineering decision is to replace the operation, not offload the loop.

## Slide 7
STEP 3
Classify Each Phase
Build Matrix
Data-parallel
Every element independent. N² or bufLen entries computed in parallel. Natural GPU kernel.
Barrier / Lock
Phase gate
Ensures build is complete before solver reads. Free on GPU — stream ordering.
Cholesky Factor
Vendor library
Serial as written. Replaced by dpotrf / cusolverDnDpotrf. Small N per call.
Triangular Solve
Vendor library
Serial as written. Replaced by dpotrs / cublasDtrsm. Small N per call.
State Update
Data-parallel
Element-wise feedback into buffer. Natural GPU kernel.

## Slide 8
THE TRAP
Per-Iteration Analysis Gives the Wrong Answer
The per-iteration triage says: build phase is a good kernel, but the solver is too small. cuSOLVER at this N loses to MKL.
The per-iteration crossover says: CPU wins below N ≈ 400–512. Your matrix is below crossover. Do not offload.
This conclusion is correct for a serial recurrence — where you are stuck running one small Cholesky at a time.
But your outer loop iterations are independent. You are not stuck with one small problem. You have thousands of small problems.
Graph replay does not fix this. Replaying one slow kernel 50,000 times via a CUDA graph means you lose 50,000 times with slightly less launch overhead per loss. The graph optimizes the wrong thing.

## Slide 9
THE KEY INSIGHT
Batch Across Iterations
Instead of one 224×224 Cholesky per stream submission, batch all K independent Choleskys into a single operation.
cusolverDnDpotrfBatched — factor K matrices simultaneously. Every SM has work.
cublasDtrsmBatched — solve K independent triangular systems in one call.
buildMatrix becomes one kernel across all K matrices — each GPU thread computes one element of one matrix.
updateState becomes one kernel across all K state vectors.
At N=224, one dpotrf gives the GPU ~3.7 MFLOP — far too little. But 50,000 batched dpotrf calls give the GPU ~185 GFLOP of independent work. That fills the device.

## Slide 10
BATCHED EXECUTION
GPU Model — K Iterations Batched
Kernel: buildMatrix × K
K·N² threads — all matrices built in one launch
cusolverDnDpotrfBatched
K independent factorizations — every SM has work
cublasDtrsmBatched × 2
K independent forward + backward solves
Kernel: updateState × K
K state vectors updated in one launch
Four launches total for K iterations. All K matrices stay in device memory.
Compare: per-iteration graph replay = 4K launches for K iterations.
Batching changes the GPU from "one small problem on 80 SMs" to "K small problems distributed across 80 SMs." K = 50,000 fills the device at any N.

## Slide 11
STEP 6
The Crossover Shifts with Batching
Outer Loop | Per-Iteration N | GPU Strategy | Outcome
Serial recurrence | Small | Graph one iteration | CPU wins
Serial recurrence | Large | Graph one iteration | GPU wins above crossover
Independent iterations | Small | Batch across iterations | GPU wins if batch fills device
Independent iterations | Large | Single iteration saturates | GPU wins easily
Row 3 is the case most often missed.
The per-iteration triage says "too small for GPU." The batch triage says "50,000 small problems is not a small problem." The deciding factor is not per-iteration arithmetic density — it is total batch arithmetic density.

## Slide 12
STEP 6
Three CPU Baselines to Beat
If the production code has OpenMP + locks, there are three baselines — not one:
1
Lock-contested OpenMP
Production code as-is.
Artificially slow — threads
waiting on locks, not computing.
2
Single-threaded, no locks
True serial cost per iteration.
What one GPU stream must beat.
3
OpenMP with locks fixed
The fair fight.
This is the real CPU baseline
the batched GPU must beat.
Comparing the batched GPU against baseline 1 overstates the GPU win. Comparing against baseline 3 is the fair fight. Often, fixing the mutex pattern on CPU alone is the bigger speedup.

## Slide 13
STEP 7
Orchestration: Batch First, Graph Second
With independent iterations, the orchestration priority inverts. Batching is the first-order optimization, not graphs.
Batch the build kernels: one launch builds all K matrices. Batch the factorizations: one cusolverDnDpotrfBatched call. Batch the solves.
Graph capture can then wrap the batched sequence: four launches total captured into one graph. Graph replay adds incremental value on top of the batched execution.
A graph replaying unbatched iterations is 4K launches. A graph replaying batched iterations is 4 launches. Batch first.
Memory: K matrices × N² × 8 bytes must fit in device memory. At K=50,000 and N=224, that is ~19 GB. If it does not fit, batch in chunks.
Kernel quality first. Batching second. Graph capture third. Launch count last.

## Slide 14
STEP 8
Profile the GPU Side
Nsight Systems
Timeline: launches, gaps, sync, overlap, stream activity, graph replay.
Is orchestration the problem?
Nsight Compute
Per-kernel: occupancy, memory throughput, arithmetic throughput, stalls, warp divergence.
Is the kernel the problem?
A slow batched GPU result is not a conclusion. The profiler tells you where the time is going — feed back into the batch sizing and kernel design.

## Slide 15
The Decision Ladder
0
Read the code. Verify iterations are independent. Classify every lock.
1
Strip OpenMP + locks. Profile one iteration single-threaded. Measure build vs solver split.
2
Replace the solver with a vendor library call. MKL on CPU, cuSOLVER on GPU.
3
Classify: build = data-parallel kernel. Barrier = free. Solver = vendor library. Update = data-parallel kernel.
6
Per-iteration crossover says CPU wins at small N. But iterations are independent — proceed to batching.
→
Batch across iterations. cusolverDnDpotrfBatched, cublasDtrsmBatched, fused kernels.
7
Graph capture the batched sequence. Four launches total, not 4K.
8
Profile the GPU side. Nsight Systems for orchestration, Nsight Compute for kernels. Feed back.

## Slide 16
Replace operations, not loops.
Classify every lock before assuming parallelism.
Use vendor libraries for the math.
Batch independent iterations — do not graph them one at a time.
Measure the crossover against the optimized CPU.
50,000 small problems is not a small problem.