## Slide 1
HOW WE GOT HERE – A HISTORY OF GPU COMPUTING
Why this matters for you
Sections 8–9 — the pendulum, and the practice it explains
1982–1999
Fixed function
SGI’s pipeline · GeForce 256 freezes T&L and coins “GPU”
COMPUTATIONAL STYLE
CONFIGURE THE PIPELINE
state settings, no programs
2001–2016
The great opening
Shaders → Brook → CUDA — the machine becomes general
COMPUTATIONAL STYLE
WRITE THE KERNEL
one function, many independent elements
2017–now
The pendulum returns
Tensor cores · RT cores · the heterogeneous machine
COMPUTATIONAL STYLE
ORCHESTRATE THE UNITS
kernels + libraries feeding frozen silicon
Closing seminar · the last two sections, and every rabbit hole they were secretly about
Notes: Framing: every seminar so far presented a rabbit hole. Tonight the main scroll catches up with them - Sections 8 and 9 are where the holes converge. The three rows are the whole arc in one breath.

## Slide 2
SECTION 8 · THE PENDULUM
The whole history is one motion
1983–99
Fixed function
SGI’s pipeline;
GeForce 256 freezes T&L (1999)
2000–01
Programmable
DirectX 8 shaders;
GeForce 3 opens the pipeline
2006
Fully general
CUDA on G80 — 128 unified
cores, one pool
2017–18
Fixed returns
Tensor cores (Volta);
RT cores (Turing)
Today
The mixture
General + tensor + RT,
side by side in each core
One mechanism, repeating. When an operation becomes dominant and stable, it gets frozen into silicon; when workloads shift, generality returns. Fixed-function and general-purpose are not stages the field passes through — they are the two ends of a pendulum, and the swing is driven by economics.
Notes: Recap slide - the audience has seen all of this in pieces. The point is the shape: one motion. Every prior seminar sits somewhere on this line.

## Slide 3
SECTION 8 · THE PENDULUM
When it pays to freeze an operation
Generality is never free. A programmable core spends transistors and energy on flexibility — fetching and decoding instructions, scheduling, deciding what to do next. When a single operation comes to dominate the workload, all of that apparatus of choice is overhead spent doing the same thing over and over.
DOMINANT
The operation owns the workload — most cycles, most energy, most of what the machine is bought to do.
STABLE
It will not change underneath the silicon. A frozen circuit cannot be patched; freeze too early and the workload walks away from it.
FEEDABLE
The memory system can keep the circuit busy. Most operations starve at the memory’s pace — the rabbit holes explain the one that does not.
1999: the GeForce 256 froze transform & lighting and the word “GPU” was coined. 2017: the same logic, applied to a new operation. The principle never changed — only the operation worth freezing did.
Notes: The third card (FEEDABLE) is the rabbit-hole contribution - the main text gives two conditions, the tensor-core note adds the third. It pays off two slides from now.

## Slide 4
SECTION 8 · THE PENDULUM
The T&L bargain again — tensor cores, 2017
WHAT VOLTA FROZE
D = A·B + C on 4×4 tiles
64 multiply-accumulates as one hardware step — no instruction fetched, no scheduling decision per multiply. The wiring is the algorithm.
V100 (2017): 640 units beside the general cores — up to ~12× on the same arithmetic.
Half-precision products, wider accumulation: rounding compounds over thousands of terms, so the sum is carried wide.
Large matrices reach it by tiling — block matmul is still matmul; nothing is lost.
N
WHAT IS A TENSOR CORE? · §8 NOTE
Why matmul is the one you can feed
n³ ops on n² data
Every value fetched from memory is reused n times. Moving data is the hidden cost of the whole platform (Lesson 4) — and the matrix multiply is the rare operation whose arithmetic grows faster than its appetite for data. Freeze almost anything else and the circuit starves at the memory’s pace. Freeze this, and the arithmetic outruns the traffic.
“It is the transform-and-lighting unit’s bargain again, with the matrix multiply in the place of geometry.”
Notes: The blue N chip is the document's own note button - this is the Section 8 note added this week. If anyone wants the precision story or the tiling detail, open the note live.

## Slide 5
SECTION 8 · THE PENDULUM
The math, written out — one MMA tile (2×2 for space)
D
[d11 d12]
[d21 d22]
A
[a11 a12]
[a21 a22]
B
[b11 b12]
[b21 b22]
C
[c11 c12]
[c21 c22]
=
·
+
ALL OF IT — NOTHING HIDDEN
d11 = a11·b11 + a12·b21 + c11
d12 = a11·b12 + a12·b22 + c12
d21 = a21·b11 + a22·b21 + c21
d22 = a21·b12 + a22·b22 + c22
THE COUNT AT n = 2
8 multiply-accumulates, 16 arithmetic ops, from 12 inputs. Every element of A and B appears twice — reused n times. That reuse is the feedability.
THE REAL UNIT: n = 4
64 multiply-accumulates — sixteen boards like this one, four terms per line instead of two. A tensor core executes ALL of it as one indivisible step.
No loop, no instructions, no schedule — these equations ARE the circuit. The wiring is the algorithm.
Notes: The demystifying slide: a tensor core is not exotic - it is exactly this arithmetic, hardwired. Walk one line aloud (d11 takes A's row 1 against B's column 1, plus the accumulator). Point at the reuse: a11 appears in two equations - at n=4 each value appears four times, which is the n-squared-data / n-cubed-work argument made visible. In half precision the products are computed narrow; the + before c is done wide - that is the precision bargain on the previous slide.

## Slide 6
SECTION 8 · THE PENDULUM
Tiling — an 8×8 slides through the 4×4 unit
D
D11
D12
D21
D22
each block = one 4×4 tile
A
A11
A12
A21
A22
each block = one 4×4 tile
B
B11
B12
B21
B22
each block = one 4×4 tile
C
C11
C12
C21
C22
each block = one 4×4 tile
=
·
+
THE COUNT
4 blocks
× 2 passes
= 8 MMA steps
= 512 MACs
= 8³ exactly
D12 = A11·B12 + A12·B22 + C12
row 1 of A against column 2 of B — block algebra is ordinary matrix algebra, one level up (compare the d12 line on the previous slide)
PASS 1 · ONE MMA STEP
T = A11·B12 + C12
A full 4×4 tile product plus the accumulator tile — 64 MACs, one indivisible step.
PASS 2 · THE ACCUMULATOR CARRIES
D12 = A12·B22 + T
The partial sum rides in through the +C port. That input is not decoration — it is the plumbing that lets block algebra chain.
Every matrix in the world reaches the unit this way: an N×N multiply is (N/4)³ tile steps. A transformer layer is this picture, thousands of tiles deep — the schedule changes; the arithmetic never does.
Notes: The bridge slide between the written-out 2x2 and the real workload. Walk it: to build the upper-right block of D you sweep row 1 of A against column 2 of B - the same row-against-column rule as scalars, one level up. Each block product is ONE tensor-core step (the previous slide, sixteen boards at once); the running sum is carried by the +C accumulator port between passes - emphasize that the accumulator input exists in the hardware precisely so tiles can chain. Count check: 4 result blocks x 2 passes = 8 MMA steps x 64 MACs = 512 = 8 cubed. At half precision the products are narrow and T rides wide - the precision bargain protects exactly this running sum.

## Slide 7
SECTION 8 · THE PENDULUM
Who orchestrates the blocking?
THE LIBRARY KERNEL
software — written and autotuned per architecture by the vendor
cuBLAS / cuDNN kernels decide everything: which thread block owns which region of D, the tile sizes, the sweep order, and when tiles stage from main memory → shared memory → registers. The choreography, not the arithmetic, is the hard part — it is what Lesson 3 buys.
▼
THE HARDWARE SCHEDULERS
silicon — the SM’s own machinery
The global scheduler sprays thread blocks across SMs; each SM’s warp schedulers interleave the streams — one warp waits on a tile from memory while another fires its MMA. The MMA instruction is warp-wide: the tile’s operands live spread across the warp’s registers.
▼
THE TENSOR CORE
frozen — the bottom of the stack
Eats one tile operation when a warp hands it one. That is all it does. The unit is deliberately dumb; the intelligence lives in the schedule above it.
WHAT THE SCHEDULE REALLY IS
A data-residency design. Each tile of A is loaded into fast shared memory once and reused against many tiles of B before eviction — the n³-on-n² reuse, made physical. The orchestration exists to protect the feedability. Lessons 3 and 4 are one lesson, seen from software and from hardware.
ONE LEVEL UP: THE FRAME
Same answer at frame scale: the game and driver record the command stream — ray pass, shade pass, DLSS pass — and every intermediate stays resident on board. Nothing crosses the bus between passes.
At every scale, the same division of labor: general silicon does the deciding; frozen silicon does the doing.
Notes: Answers the question the tiling slide raises. Three layers: the library kernel is the strategist (this is the real content of Lesson 3 - you are not buying multiplications, you are buying a data-movement schedule that took experts months); the SM schedulers are the executors (warp-wide MMA, latency hiding by interleaving); the tensor core is deliberately dumb. Right cards: the schedule IS a residency design (Lesson 4), and the frame-level version is the same pattern. The closing line is the heterogeneous machine in one sentence - it also sets up the DLSS and heterogeneous slides ahead.

## Slide 8
SECTION 8 · THE PENDULUM
Where does D get put back together?
Nowhere — and that is the design. Decomposition and recomposition are addressing, not operations. The blocks are a coordinate system imposed on the matrix — never a transformation applied to it. Nothing is split going in; nothing is glued coming out.
THE K-DIRECTION: RECOMPOSED IN REGISTERS
pass 1: T = A11·B12 + C12
pass 2: D12 = A12·B22 + T
store: D12 → global memory (once)
The accumulator tile stays resident in the warp’s registers across the whole sweep — the +C port chains passes inside the register file. Nothing partial ever touches memory.
THE SPATIAL LAYOUT: RECOMPOSED BY ADDRESSES
D lives in global memory as one flat array, allocated once. Thread block (i, j) owns rows 4i…, columns 4j… by coordinates, and stores its finished tile straight to those addresses. Memory layout is the glue: no merge pass, no gather, nobody whose job is reassembly. A blocked matrix is a VIEW over one array — mdspan’s word for it — never a copy.
WHY THIS IS FORCED, NOT CLEVER
Writing the output is n² stores against n³ arithmetic — asymptotically free, provided each element is written exactly once. Materialize intermediate blocks and re-merge them, and you pay n³-scale memory traffic: precisely the cost the whole architecture exists to avoid.
Split is index math on the way in; glue is index math on the way out — the data never learns it was blocked. Lesson 4, stated negatively: the fast matmul only ever writes its result, never revisits it.
Notes: Answers the natural misconception that blocks are physically taken apart and glued back. Two recompositions, neither a step: the K-direction partials chain in the register file via the +C accumulator port (T never touches memory; one store when final), and the spatial layout reassembles by store addresses into the one flat D array (blocking is a view, not a copy - the mdspan concept). The cost argument makes it forced: n-squared stores are free against n-cubed work only if written once. Good Q&A comeback: 'the questioner who asks this is one index-arithmetic sentence away from understanding the whole machine.'

## Slide 9
SECTION 8 · THE PENDULUM
What if you need the result back?
Then you pay the bus, and the accounting changes. The inputs cost 2n² values going over; D costs n² coming home — against the n³ arithmetic that earned it. An isolated round-trip matmul does only ~n/3 operations per value moved: large matrices amortize the trip, small ones drown in it. (Illustrative: at ~50 GB/s of bus and ~50 TFLOP/s of compute, the one-shot break-even sits at n in the thousands.)
THE NEXT COMPUTE NEEDS D
Then do not bring it back. Chain the next kernel — D stays resident and becomes the next A. This is the common case: a network layer’s output feeds the next layer; a solver’s iterate feeds the next sweep. Lesson 4’s rule, applied.
bring back: nothing
YOU NEED A SUMMARY OF D
Then reduce on the device: a norm, a residual, a convergence check, a yes/no. Ship one number home instead of n² — the bus should carry conclusions, not data.
bring back: one number
YOU GENUINELY NEED ALL OF D
Then pay the n² — but hide it: asynchronous copies of finished tiles overlap the compute of the remaining ones (streams, pinned memory), so the trip pipelines behind the arithmetic. And if one small matmul is the whole job: do not offload — the CPU wins that race.
bring back: n², overlapped
THE DISCIPLINE IS ALREADY IN THE API
cuBLAS takes device pointers and leaves D where it made it — copying back is a choice you make explicitly, never a default. And this is the offload guide’s whole question asked of one operation: count arithmetic per byte across the BUS, not per byte of DRAM.
Bring home conclusions, not matrices — and when you must bring the matrix, hide the trip under the math.
Notes: Completes the matmul arc by crossing the bus. The break-even arithmetic behind the illustrative claim: transfer 3n^2 x 4 bytes at ~50 GB/s vs 2n^3 flops at ~50 TFLOP/s -> equal near n ~ 6000; below that a one-shot round trip is transfer-dominated (numbers are order-of-magnitude, hardware-dependent - say so if pressed; the companion Roofline lab is where they measure it themselves). The three cards are a decision tree the audience can reuse: chain / reduce / overlap. cuBLAS's device-pointer API is the cultural artifact: the library's signature teaches residency.

## Slide 10
SECTION 8 · THE PENDULUM
The triangle returns — RT cores, 2018
WHAT THE RT CORE COMPUTES — EXACTLY
BVH traversal: walk a tree of nested bounding boxes with ray–box slab tests, discarding whole subtrees the ray misses — one triangle found among millions in ~log n steps.
Then, per surviving candidate triangle, one small linear solve:
O + t·D = (1-u-v)·V0 + u·V1 + v·V2
ray origin O, direction D — solve for (t, u, v): cross and dot products, hardwired
t is the hit distance; (u, v) are barycentric coordinates — the very coordinates Section 1 interpolates attributes with. A 3×3 solve, cast in silicon: the undercarriage in miniature.
Frozen for the ORIGINAL customer — graphics itself — where the tensor core froze the NEW one (AI). Turing 2018; every SM: CUDA + tensor + RT.
THE LONGEST CALLBACK IN THE DOCUMENT
Section 1: the triangle wins because every pixel can be decided independently — the rasterization bargain.
1995: the NV1 refuses it, bets on quadratic patches, and nearly kills the company. Direct3D makes the triangle the format.
2018: the same primitive earns its own dedicated silicon all over again.
“The shapes the story keeps returning to are the shapes worth casting in hardware.”
— and the NV1’s curved patch got its own vindication: the tessellator stage now evaluates BernsteinBasis(u) in every Direct3D 11 pipeline.
Notes: Wrong turns matter: the NV1 is the document's canonical wrong turn, and it comes back twice - as the triangle's victory here, and as the patch's vindication in the tessellation stage (From Weierstrass to the GPU note). Key contrast to say aloud: tensor cores serve the workload that arrived from outside (AI); RT cores serve graphics itself - the machine that went general for compute simultaneously re-froze its own original job. Bonus synergy if asked: the two frozen units cooperate in practice - ray-traced frames are denoised/upscaled by neural nets running on the tensor cores (DLSS), so graphics now consumes the AI silicon too.

## Slide 11
SECTION 8 · THE PENDULUM
Tessellation — you have been watching it
Tessellation is cutting a smooth, exactly-described surface into flat triangles the rasterizer can draw. A patch is a compact exact description (9 control points, 27 floats); the rasterizer only eats triangles; tessellation converts one into the other — on the fly, every frame.
HULL SHADER
programmable
Decides HOW FINELY. A patch filling the screen gets thousands of triangles; a distant one gets four. Your animation’s rule — subdivide until the flat-triangle error is invisible — is this stage’s job.
TESSELLATOR
fixed function — the frozen part
Decides WHERE to sample. Generates the (u,v) sample points in the parameter square and their triangle connectivity. Pure combinatorics — it never knows what shape the surface is.
DOMAIN SHADER
programmable
Decides WHAT the surface says there. Evaluates the patch equation at each (u,v) — for a Bézier patch, a weighted sum of control points with BernsteinBasis weights — producing the real 3D vertex.
N
WHAT IS A QUADRATIC PATCH? · §2 NOTE
You have watched tessellation all semester: the first patch animation’s right half — the same surface re-drawn as a triangle mesh, denser wherever curvature demands, 27 floats beside hundreds — and the fillet tiled by flying triangles. Those animations ARE this process. Today it gets its name, and its own frozen stage.
The patch is the description; the triangle is the drawing primitive; tessellation is the bridge — and its heart is fixed-function. The pendulum, again.
Notes: The vocabulary slide - deliberately placed before the patch's-revenge timeline, which assumes the word. The seminar moment: 'you have known this concept for months; the right half of the very first animation IS tessellation - today it gets its name.' The three-stage split is the same division of labor as the whole machine: programmable stages decide (how finely, what shape), the frozen stage executes (where to sample, pure combinatorics). Adaptive detail in your cvQuad animation (triN chosen by curvature tolerance) maps to the hull shader's level-of-detail decision.

## Slide 12
SECTION 8 · THE PENDULUM
The patch’s revenge — curves return to silicon
N
FROM WEIERSTRASS TO THE GPU · §2 NOTE
1992
SGI RealityEngine
Evaluated patches in hardware (control points → surface points on the Geometry Engine) — but still rasterized triangles. “Evaluate, then tessellate.”
1995
NVIDIA NV1
The radical version: rasterized the patch ITSELF — no triangles anywhere. Direct3D chose the triangle; the NV1 failed and nearly took the company with it.
2001
ATI TruForm (Radeon 8500)
First consumer GPU with an on-chip tessellator (N-patches). Right idea, wrong decade — almost no adoption.
2005
Loop–Blinn
Bézier curves rasterized directly in the pixel shader — resolution-independent fonts and vector art on the GPU.
2009–10
Direct3D 11 · OpenGL 4
Tessellation becomes a standard stage: hull shader → fixed-function tessellator → domain shader. The domain shader evaluates BernsteinBasis(u) per vertex.
WHERE THE PATCH LIVES NOW
HULL SHADER
programmable — sets patch detail
▼
TESSELLATOR
FIXED FUNCTION — splits the patch
▼
DOMAIN SHADER
programmable — evaluates
BernsteinBasis(u, v) per vertex
▼
RASTERIZER
fixed function — triangles, as ever
The NV1 was wrong by one pipeline stage, not wrong in kind: the triangle kept the rasterizer, and the curve got its own stage upstream. Every modern pipeline evaluates Bernstein polynomials in hardware — the 1912 coin-flip weights, per vertex, per frame.
Notes: This is the hardware half of the 'one rabbit hole, end to end' slide - the math lineage ran Weierstrass to PostScript; this runs SGI to D3D11. All dates per the document's VERIFIED CLAIM #14 (SGI evaluate-then-tessellate vs NV1 rasterize-the-patch is the load-bearing distinction; TruForm Aug 2001 first consumer HW tessellation; Loop-Blinn SIGGRAPH 2005; hull/tessellator/domain standard ~2009-10, Microsoft's own SimpleBezier11 sample calls BernsteinBasis(u)). The kicker to say aloud: the wrong turn was a timing error, not a concept error - and the vindicated concept re-entered the pipeline as a FIXED-FUNCTION stage, which is the pendulum again.

## Slide 13
SECTION 8 · THE PENDULUM
Two frozen units, one frame
GENERAL CORES
The game’s shader casts rays — only a few per pixel. A full path trace would blow the ~16 ms frame budget many times over.
▼
RT CORES
Per ray: walk the BVH, solve the ray–triangle system → where the light lands. Millions of hit points per frame, in fixed-function silicon.
▼
GENERAL CORES
Shade the hits — materials, lights, bounces. The result is honest but NOISY and low-resolution: truth, sparsely sampled.
▼
TENSOR CORES
Neural denoise + upscale (DLSS). Inference is matrix multiplies — the network reconstructs the pixels and rays that were never cast.
▼
DISPLAYED FRAME
Film-quality light at game frame rates. Neither unit could deliver it alone.
WHY A NETWORK, NOT MORE RAYS
Every extra ray costs as much as the last one. Reconstruction costs a fixed inference budget, on silicon that would otherwise sit idle. Casting few rays and inferring the rest beats casting enough — the economics chose this architecture. Lesson 5’s dial, applied to light.
THE DEPENDENCY RUNS BOTH WAYS
The RT core’s output is exactly what the network needs — sparse, honest samples of the light field. The network is exactly what the RT core needs — a way to be affordable in real time. Neither frozen unit could ship real-time ray tracing alone.
The operation that left home to serve compute came back to serve the pictures — graphics now consumes the AI silicon. The frozen units do not just coexist; they feed each other.
Notes: The cooperation slide. DLSS = Deep Learning Super Sampling, running on the tensor cores (established since the Turing whitepaper; specific DLSS version details are deliberately not on the slide - the mechanism is the point). Walk the flow top to bottom: cast few - hit exactly - shade honestly - reconstruct the rest. The right cards carry the two arguments: the economics (rays cost linearly, inference is a fixed budget) and the mutual dependency. This slide sets up the heterogeneous machine slide that follows: the units are not just side by side, they are a supply chain.

## Slide 14
SECTION 8 · THE PENDULUM
The pendulum settles into a mixture
ONE MODERN GPU CORE (SM)
GENERAL CORES
The shader-and-CUDA inheritance. Stay because new workloads keep arriving and something has to run them.
TENSOR CORES
The matrix multiply, frozen. Dominant, stable, and the one operation the memory system can keep fed.
RT CORES
Ray ∩ triangle, frozen. The document’s first primitive, back in dedicated silicon.
Special-purpose and general-purpose are a portfolio, not a sequence. The general core is the bet on workloads that do not exist yet; the fixed units are the profits taken on the ones that proved dominant and stable. Expect the portfolio to be rebalanced — that is what the whole history says it is.
Notes: This is where Section 8 lands. From here, pivot: 'so what does a machine shaped by THIS history demand from your code?' - Section 9.

## Slide 15
THE RABBIT HOLES · WHERE THEY ALL LANDED
Everything converges on linear algebra
N
THE UNDERCARRIAGE · QUADRATIC-PATCH NOTE, FINAL SECTION
THE CLAIM
The only equations we can really solve are linear. Nonlinear problems are solved as sequences of linear ones — Newton, gradient descent, every solver in the catalogue.
Backpropagation is the chain rule; the chain rule is products of Jacobians; products of Jacobians are matrix multiplies.
Graphics is matrix arithmetic. Simulation is matrix arithmetic. Learning is almost nothing but the matrix multiply.
THE PAYOFF
1999 → matrix × vector
2017 → matrix × matrix
The pendulum’s two endpoints froze the same mathematics twice. What changed is the shape of the operands and what the numbers mean. The operation — a weighted sum of weighted sums — never did. This is why one machine serves graphics, simulation, and AI: they were always the same customer.
“The patch, the pipeline, and the silicon are three views of the one operation we actually know how to perform.”
Notes: This is the seminar's thesis: the rabbit holes were never digressions. The deepest note predicted what the hardware did - the industry poured the undercarriage claim into silicon.

## Slide 16
THE RABBIT HOLES · THE DEEPEST CLAIM, EXAMINED
The claim, stress-tested
“The only equations we can really solve are linear. Nonlinear problems are solved as sequences of linear ones.”
A thesis, not a theorem — like Church–Turing: unprovable, compressing a survey of practice, earning its keep by surviving counterexamples.
QUADRATURE IS LINEAR
Integration is a linear operation. Every ODE “solved by quadrature” — the oldest solvability there is — is a reduction to applying a linear functional.
ROOTS ARE EIGENVALUES
Polynomial root-finding, the ur-problem of algebra, is solved in practice by building the companion matrix and calling an eigenvalue routine. The oldest nonlinear problem became a linear-algebra call.
THE FFT IS A LINEAR MAP
The most-used algorithm in signal processing is nothing but a fast change of basis. The spectral world runs entirely on superposition.
EVEN THE ESCAPE IS LINEAR
A neural network puts ALL coupling between variables in its linear maps; the nonlinearity is deliberately pointwise and cheap. Our universal nonlinear solver is, by FLOP count, almost entirely matrix multiplication.
Judged as a thesis: about ninety percent true — and the remaining ten percent is the interesting part. Next slide.
Notes: Position the claim in its correct genre first - a Church-Turing-style thesis, judged by whether counterexamples survive. The four evidence cards are supports the audience may not have noticed: quadrature IS applying a linear functional; MATLAB's roots() literally builds a companion matrix and calls eig; the FFT is a change of basis; and network architecture itself obeys the claim (all interaction in the matrices, nonlinearity pointwise where it is embarrassingly parallel). Even our escape from linearity is built out of linearity.

## Slide 17
THE RABBIT HOLES · THE DEEPEST CLAIM, EXAMINED
The honest ten percent
CONVEXITY
A genuinely distinct certificate: local = global, separating hyperplanes, duality. Not reducible to linear algebra — the document corrected itself on exactly this point.
CONTRACTION & ORDER
Banach fixed points, value iteration, monotone convergence — proofs by metric and order geometry, with no linearization anywhere in the argument.
LOGICAL STRUCTURE
A SAT solver really solves NP-complete instances and emits a certificate — by resolution, not superposition. The discrete world has its own laws.
THE REFINEMENT: WHERE THE PROOFS LIVE vs WHERE THE FLOPS LIVE
Convexity signs the warranty — but interior-point runs Newton systems inside. Contraction guarantees convergence — but each sweep, in practice, is matrix multiplies. Integrable systems solve by hidden linearization. Several structures make problems PROVABLY solvable; only one is COMPUTABLE at scale, and the others route their inner loops through it. Linear algebra does the work; the other structures sign the warranty.
AND THE CLAIM IS GETTING TRUER — BY CONSTRUCTION
The tensor core froze matmul because everything routes through it; now algorithms reshape themselves to feed the frozen unit. “Solvable” has always meant “reducible to what our instruments perform” — and we have built planetary-scale instruments for exactly one operation. The pendulum, operating on mathematics itself.
Concede the taxonomy, keep the thesis: scoped to the continuum, no counterexample survives.
Notes: The concessions make the thesis stronger, not weaker - it has now been stress-tested. If a logician raises SAT, congratulate them: they have found the one kingdom where the writ of linearity does not run, and it happens to be theirs (resolution proofs are real certificates with no superposition anywhere). The claim as written is about EQUATIONS - continuous mathematics - where no counterexample survives the proofs-vs-FLOPs refinement. The reflexivity card is the seminar's most philosophical beat: the thesis has a feedback loop with the silicon (QUDA bending its multigrid toward tensor cores is the live example); it is partly a fact about us and our instruments, not only about mathematics - Descartes reduced geometry to algebra because algebra was what his tools did.

## Slide 18
THE RABBIT HOLES · THE METHOD, DEMONSTRATED
One rabbit hole, end to end
N
FROM WEIERSTRASS TO THE GPU · §2 NOTE
1872–85
Weierstrass
The nowhere-differentiable monster — then the theorem: every continuous curve can be shadowed by a polynomial. Existence only; no construction.
1912
Bernstein, Kharkov
A two-page probabilistic proof. The weights are binomial probabilities — the polynomials are born as a coin-flip distribution.
1959
de Casteljau, Citroën
Repeated linear interpolation turns car bodies into equations — kept secret, so the curves take Bézier’s name.
1972–
Forrest · PostScript
The industrial curves are recognized as Bernstein polynomials; every rendered glyph becomes one.
2001–10
TruForm → D3D11
Tessellation returns curves to hardware: the domain shader evaluates BernsteinBasis(u) per vertex — the NV1’s idea, one stage later.
A question about one animation — “what is a quadratic patch?” — descended to 1912 probability and surfaced inside the silicon. That is what the rabbit holes are for.
Notes: The method slide. One curiosity thread, followed honestly, crossed four department boundaries and ended at the hardware. No course crosses these lines - that is the argument for the method itself.

## Slide 19
SECTION 9 · WHY THIS MATTERS FOR YOU
Lesson 1 — It is a throughput machine
1
THE HISTORY THAT EXPLAINS IT
Gaming economics built it: millions of $300 cards, not thousands of $100k workstations — the volume flywheel from Section 2.
A frame is millions of independent pixels; latency on any one of them is irrelevant. The silicon inherited that: thousands of small, slow, simple cores.
Nothing about CUDA changed the economics — compute rides on hardware shaped by games.
THE PRACTICE IT DEMANDS
The first question of any port is not “how fast is the GPU?” but “is there enough parallel work to be worth the trip?”
Small or serial work loses — not by a little, by orders of magnitude. One fast core beats a thousand slow ones on a serial problem.
Throughput-over-latency is not a setting. It is the machine.
The machine is a consequence of who paid for it. Program the economics, not the brochure.
Notes: Lesson slides all follow: history left, practice right. This one is the foundation - everything else assumes the audience accepts throughput-over-latency as baked in.

## Slide 20
SECTION 9 · WHY THIS MATTERS FOR YOU
Lesson 2 — The programming model is the hardware
2
THE HISTORY THAT EXPLAINS IT
Section 1’s bargain: every pixel decided independently. The model was always there — one function over many independent elements.
Section 4’s hacks proved it: floats disguised as pixel colors, matrices as textures — general compute forced through a graphics-shaped hole.
Brook (2004) named it — streams and kernels — and CUDA (2006) made it the native tongue.
THE PRACTICE IT DEMANDS
Data-parallel code ports almost by transcription: one kernel, many elements, no cross-talk.
Deeply serial code must be rethought, not translated. If element i needs element i−1, you are fighting the machine’s founding assumption.
Ask of every loop: are the iterations strangers to each other?
N
MATRIX ADDITION AS PIXELS · §4 NOTE
CUDA did not invent the model — it stopped requiring the disguise. The hardware’s shape was the model all along.
Notes: The matrixAddition rabbit hole (floats packed into RGBA texels) is the visceral proof that the model predates the API. Open it if anyone doubts the 'disguise' framing.

## Slide 21
SECTION 9 · WHY THIS MATTERS FOR YOU
Lesson 3 — Call a library, not a kernel
3
THE HISTORY THAT EXPLAINS IT
Section 5’s bet: the integrated proprietary stack — CUDA plus its libraries — beat the open alternative that shipped as a spec.
cuBLAS, cuFFT, cuSOLVER, cuDNN: vendor kernels tuned per architecture, by the people who designed the silicon.
When tensor cores arrived in 2017, code that called the libraries got them for free — without changing a line.
THE PRACTICE IT DEMANDS
Hand-written kernels lose to vendor libraries on the operations that matter — and age worse with every hardware generation.
Write to the operation, not the device: say “multiply these matrices,” let the library choose the silicon.
Your own kernels are for the glue between library calls — not the linear algebra inside them.
N
THE RUNWAY AND THE PLANE · §7 NOTE
The library is the contract that outlives the hardware. It is also the only door to the tensor cores.
Notes: cudaLuck callback: the libraries were the runway. AlexNet was the plane. Deliberate skill was recognizing the landing within months - cuDNN 2014, DGX, the pivot.

## Slide 22
SECTION 9 · WHY THIS MATTERS FOR YOU
Lesson 4 — Moving data is the hidden cost
4
THE HISTORY THAT EXPLAINS IT
The GPU is a coprocessor across a bus — Section 6’s HPC skeptics said exactly this, and they were right; it just was not fatal.
Tianhe-1A and Titan won by keeping data resident on the device, not by shuttling it per operation.
The exception proves the rule: matmul’s n³-on-n² is why it can be frozen at all (Slide 4).
THE PRACTICE IT DEMANDS
Arithmetic per byte moved must pay for the move. Count it before you port — this is the roofline question.
Keep data resident: chain operations on the device; the worst pattern is transfer–compute–transfer per step.
A kernel that is “slower than the CPU” is usually a transfer problem wearing a compute costume.
The bus never got fast enough to stop mattering. Every fast GPU program is, first, a data-residency design.
Notes: This is the bridge to the Roofline Simulator companion - the measurement discipline lives there. The HPC-objection framing gives the skeptics their due (expertResistance pattern).

## Slide 23
SECTION 9 · WHY THIS MATTERS FOR YOU
Lesson 5 — Small costs; priced precision
5
LAUNCH OVERHEAD · THE HISTORY
Each kernel launch costs microseconds of host round-trip — invisible once, ruinous a million times.
The fixes are structural: batch the work, fuse the kernels, capture-and-replay the whole graph (CUDA Graphs).
PRECISION · THE PRICE LIST
FP64 on consumer cards: 1:8 → 1:24 → 1:32 → 1:64 of FP32, generation by generation — a business decision, not physics (Section 6).
Tensor cores dial the other way: FP16 → INT8 → INT4 — precision engineered as a spectrum, priced by the workload.
Choose precision like you choose an algorithm: deliberately, and check what your card actually provides.
The FP64 penalty in the offload guide is a price list, not a law of nature. Read the price list before you design.
Notes: Two independent small-print lessons on one slide. The 1:8-to-1:64 sequence is verified in the document's claims ledger (#21); the EULA moment (2017, legal limit replacing technical) is worth telling aloud.

## Slide 24
SECTION 9 · WHY THIS MATTERS FOR YOU
Lesson 5, continued — precision in practice
CHECK THE FP64 LINE FIRST
datacenter ≈ 1:2 · consumer 1:8 → 1:64
GPUs are not one machine. Datacenter parts run double precision at half the FP32 rate — engineering-grade FP64 at full speed. Consumer cards of the SAME generation are capped at 1:32–1:64, deliberately. If your work leans on FP64 — structural dynamics, covariance solves, anywhere conditioning bites — the card class is the first architectural decision you make. One line of the spec sheet decides the design.
16-BIT IS A MEMORY STORY, NOT AN ARITHMETIC ONE
Most kernels are memory-bound (Lesson 4). Halve the width and twice as many values arrive per fetch; the working set halves; every cache line carries double. A bandwidth-limited kernel speeds up ~2× in FP16 with no tensor cores and no new ALUs — the arithmetic was never the bottleneck. Precision is a data-movement dial first, and a compute dial second.
THE DECISION PROCEDURE
Locate the kernel on the roofline first: memory-bound or compute-bound? (The companion lab exists for exactly this question.)
Memory-bound → cut bytes: lower the precision, then recover accuracy by iterative refinement. QUDA runs production lattice physics on 8-bit block floats inside double-precision outer solves — the sloppy inner pass is corrected by the exact outer one.
Compute-bound matmul → the tensor-core menu sets your formats. FP64-dominated → buy the datacenter part, or do not offload.
Precision is priced twice: once in silicon — the FP64 market segment — and once in bytes — the bandwidth bill. Read both price lists before you design.
Notes: The two additions: (1) FP64 is not gone from GPUs - datacenter silicon runs it at 1:2; only the consumer segment is capped (ratios per the document's verified claim #21) - so 'check the spec line' is a real design step, not paranoia. (2) The deep reason low precision wins on most kernels is bandwidth, not FLOPs: bytes halve, effective bandwidth doubles, and that pays even on hardware with no tensor cores at all. The QUDA example (8-bit block floats inside double outer solves, verified this session from the QUDA project page) shows iterative refinement making aggressive precision safe in production physics.

## Slide 25
SECTION 9 · THE PATTERNS UNDER THE LESSONS
Four patterns to carry out of the room
WRONG TURNS MATTER
The NV1’s patches, 3dfx buying its own channel, the open-spec bet against the integrated stack. Dead ends are where the real constraints become visible — study them, do not sand them out of the story.
EXPERT RESISTANCE
Toy → grudging science → the center of AI. When an established field says “not ready,” test the technical claims — and ask what the field would lose if the claims were wrong.
N
NONE OF THIS WAS HOSTILITY · §6 NOTE
THE ACCIDENT
Nobody planned AlexNet. The runway was built for one category of aircraft; the plane that landed was from that category, but no one ordered it. Skill is clearing the runway fast when it arrives.
N
THE RUNWAY AND THE PLANE · §7 NOTE
THE PENDULUM SWINGS AGAIN
Dominant + stable + feedable is a standing search query, not a one-time event. Whatever your field’s matmul turns out to be — someone is already weighing the silicon.
Notes: The meta-lessons. If the room takes one thing: the pendulum is a mechanism, and the three conditions are a checklist you can run on your own field.

## Slide 26
LOOKING FORWARD · THE LANGUAGE
C++26 — what actually lands
std::execution
Senders, receivers, schedulers — a standard answer to “where does this code run?” A scheduler names the place; a sender is composable work (then, when_all, bulk); the runtime is swappable. Adopted June 2024 (P2300); NVIDIA’s stdexec is the reference implementation, CUDA-stream scheduler included.
std::linalg
A BLAS-style linear-algebra interface over mdspan (C++23’s multi-dimensional array view): matrix_product, scaled(), transposed(), conjugated() — the ISO standard now names the matrix multiply as a first-class library operation, with room for accelerated backends underneath.
std::simd
Portable data-parallel value types — explicit vectorization for the CPU side of the machine, width chosen per target at compile time.
THE SHAPE OF IT (ILLUSTRATIVE)
auto task =
schedule(gpu_sched) // WHERE
| bulk(N, [=](auto i){
y[i] += a * x[i]; // WHAT
})
| then(reduce_step);
sync_wait(task); // WHEN
TIMELINE
2024 adopted · 2025 feature-frozen
late 2026 published · compilers trail:
most of it is still experimental today
Today’s bridge already exists: C++17 parallel algorithms offload to the GPU under nvc++ (-stdpar). C++26 extends that from algorithms to whole asynchronous pipelines.
Notes: Facts web-verified 2026-07-16: P2300 adopted June 2024; C++26 feature-complete June 2025; publication expected late 2026; stdexec (github.com/nvidia/stdexec) is the reference implementation. Code is illustrative stdexec style, not a verbatim compile. std::linalg = P1673, built on mdspan; its reference implementation comes out of the Kokkos world - same lineage as the radar companion code.

## Slide 27
LOOKING FORWARD · C++26, FEATURE BY FEATURE
std::execution — orchestration as a value
THE THREE CONCEPTS
SCHEDULER — the WHERE. Names an execution resource: a CPU thread pool, a GPU stream, an inline loop. The place code runs becomes a first-class value you pass around.
SENDER — the WHAT. A composable description of asynchronous work. Nothing runs when you build it; pipelines assemble from algorithms — then, when_all, bulk — like expressions.
RECEIVER — the way back. Results, errors, and cancellation each get a typed channel. No detached threads, no lost exceptions: structured concurrency by construction.
THE SHAPE (ILLUSTRATIVE)
auto pipe =
schedule(gpu) // WHERE
| bulk(N, step_kernel) // WHAT
| continues_on(cpu_pool) // hop home
| then(report);
sync_wait(pipe); // WHEN
WHY THIS SHAPE
Work is a value: a task graph you build, store, and launch — CUDA Graphs’ capture-and-replay idea, generalized and vendor-neutral. Retarget the entire pipeline by swapping one scheduler; the composition never changes.
Adopted June 2024 (P2300). NVIDIA’s stdexec is the reference implementation, CUDA-stream scheduler included — the orchestration layer this history invented, returning as ISO text twenty years on.
Notes: The deep idea: making work a VALUE. A sender is an object describing a computation - you can store it, compose it, hand it to a different scheduler - which is exactly what CUDA Graphs did for kernel launches, abstracted away from any vendor. The receiver channels give what raw threads never had: errors and cancellation as typed paths, so async code composes without leaks. Code is illustrative stdexec style (continues_on is the adopted name for hopping between resources). Facts verified 2026-07-16.

## Slide 28
LOOKING FORWARD · C++26, FEATURE BY FEATURE
std::linalg — BLAS becomes ISO vocabulary
WHAT IT IS
Free functions over mdspan views: matrix_product(A, B, C), norms, triangular solves — the BLAS catalogue, with standard types instead of raw pointers and leading dimensions.
mdspan (C++23) is the substrate: a non-owning view = pointer + extents + layout. A matrix, its transpose, and its sub-blocks are views over ONE array.
The adaptors — scaled(α, A), transposed(A), conjugated(A) — are views too. No copies, no data movement: just index math.
THE THEMES YOU ALREADY KNOW
Views, not copies — the recomposition slide’s lesson (blocking is addressing, never movement) encoded as API design. transposed(A) is the same array wearing different index math.
A vendor-neutral face over vendor kernels: implementations dispatch to cuBLAS, rocBLAS, MKL. Your interfaces speak standard types; the silicon underneath stays free to change.
Lineage: P1673 grew out of the Kokkos world — the same stack as the radar companion code. The people who live with portability wrote the portable interface.
The ISO standard now names the matrix multiply — the operation this whole seminar orbits — as a first-class library call. Lesson 3, ratified.
Notes: The satisfying connection: scaled/transposed/conjugated being VIEWS is the same idea as the recomposition slide - linear algebra structure lives in index arithmetic, not in data movement, and the standard API now teaches that. BLAS's raw-pointer-plus-leading-dimension interface was the de facto standard for 45 years; this is its ISO successor. P1673's reference implementation lineage runs through Kokkos (Sandia), the same ecosystem as the radar pipeline's KokkosKernels port.

## Slide 29
LOOKING FORWARD · C++26, FEATURE BY FEATURE
std::simd — one idea, three scales
WHAT IT IS
simd<T>: a register-wide pack of lanes that behaves like one arithmetic value — a + b adds every lane at once. The width is chosen per target at compile time: AVX-512, NEON, SVE.
Divergence is explicit: where(mask, x) selects the lanes that participate. You manage the pack; nothing is hidden.
The CPU side of heterogeneous code: pre- and post-processing at full memory bandwidth instead of a scalar dribble — the host keeping pace with the device it feeds.
SIMD vs SIMT — TWO FACES OF LESSON 2
std::simd — YOU manage the pack: explicit vector values on one core, widths visible, masks by hand.
GPU SIMT — the MACHINE manages the pack: thousands of threads, hardware-grouped into warps, divergence handled for you. Same discipline, opposite custody.
The founding idea appears at every scale: one function over many independent elements — lane, warp, grid. Lesson 2 is fractal: expose the independence and the width takes care of itself.
The instruction sets differ; the discipline does not. Code written as “independent elements, one function” vectorizes on the CPU, offloads to the GPU, and survives whatever width arrives next.
Notes: The teaching move: SIMD and SIMT are the same idea with custody reversed - std::simd hands you the pack, SIMT hides it in the warp scheduler. NEON/SVE in the width list quietly sets up the ARM slide two ahead. Lesson 2's 'are the iterations strangers to each other?' is the portable question at all three scales.

## Slide 30
LOOKING FORWARD · THE LANGUAGE
C++26, read with the pendulum
WHAT THE STANDARD NOW OWNS
The orchestration seam: asynchrony, task graphs, “run this there, then that here” — the streams-and-graphs layer CUDA proved, absorbed twenty years after the fact.
The interface vocabulary: mdspan for array views, linalg for the operations — standard types your APIs can speak without naming a vendor.
WHAT STAYS VENDOR TERRITORY
The kernel layer: no kernels, no memory spaces, no offload semantics in the language. CUDA, HIP, SYCL — or Kokkos above them — still write the device code.
And the pendulum says why: the hardware under that layer is still swinging (tensor cores, FP4, QPUs). You do not freeze an abstraction over moving silicon.
WHAT TO DO ABOUT IT NOW
Speak the standard vocabulary at your interfaces (mdspan today, linalg types as they land) — that code outlives every vendor cycle.
Keep orchestration migratable: stream/graph logic behind one seam, so it can move to senders when toolchains mature. Keep kernels behind libraries — Lesson 3 did not change.
std::linalg is “call a library, not a kernel” as ISO text. The standard is the fossil record of what won.
Notes: The division of labor going forward: ISO owns orchestration + vocabulary, vendors own kernels, portability layers sit between. The 'what to do now' card is the actionable takeaway for the engineers in the room.

## Slide 31
LOOKING FORWARD · THE MEMORY WALL
The ARM revolution — closing the bus
WHAT CHANGED
Lesson 4’s tax existed because CPU and GPU were separate sockets on a peripheral bus — PCIe, tens of GB/s, no shared view of memory. The trip was an artifact of packaging.
ARM licenses cores instead of selling sockets — so a system builder can put the CPU ON the accelerator’s package. NVIDIA Grace: an ARM CPU fused to the GPU over NVLink-C2C — ~900 GB/s, cache-coherent, one address space. The CPU–GPU copy becomes a cache line, not a transfer.
The consumer proof: Apple silicon — CPU and GPU on one die, one unified memory. The bus was a choice, not physics.
WHAT IT DOES NOT CHANGE
Coherence does not repeal Lesson 4. Locality still rules: HBM is still faster than the link, and a careless access pattern still starves the arithmetic.
It converts a cliff into a gradient: “transfer or die” becomes “place your data thoughtfully.” The offload guide’s questions survive; the penalties soften.
And it is not only ARM — AMD’s MI300A fuses x86 CPU, GPU, and one memory the same way. ARM’s licensing simply made custom integration the industry’s default path.
The bus is being engineered out of existence — and with it, the sharpest edge of Lesson 4. Watch for coherent links on the spec sheet: that line is the quiet revolution.
Notes: Grace/NVLink-C2C ~900 GB/s cache-coherent and Apple unified memory are established facts (pre-2026 knowledge); MI300A is the x86 counterexample that keeps the claim honest - the enabler is custom integration, which ARM's business model normalized. Presenter beat: this is the industry attacking Lesson 4 in hardware, exactly as C++26 attacks the orchestration seam in software - the pain points of the CUDA era are being engineered away one by one, which is itself evidence the lessons were the right ones. Also note NVQLink two slides ahead: the QPU link is this same movement extended to the next device class.

## Slide 32
LOOKING FORWARD · THE NEXT SWING
CUDA-Q — the stack NVIDIA is building
CUDA-Q
Single-source hybrid programs: quantum kernels (__qpu__) beside GPU and CPU code, compiled through one toolchain to simulators or real QPUs — vendor-agnostic across 17 QPU builders. The CUDA kernel model, extended to a device class the ISO standard has not imagined yet.
cuQuantum
The simulation engines: cuStateVec (state-vector) and cuTensorNet (tensor-network contraction). Both are dense linear algebra — a quantum state is 2ⁿ amplitudes, a gate is a unitary matrix, so the GPU simulates its own successor with matmul.
NVQLink
The interconnect: QPU ↔ GPU at 400 Gb/s, under 4 µs round trip, ~40 PF of FP4 on the GPU side; 5 control-system vendors; adopted by the major scientific supercomputing centers (2025).
GTC 2026
It went programmable: the cudaq-realtime API is public, and the first real-time scalable decoder for qLDPC error-correction codes ran against Quantinuum’s Helios QPU.
A QUANTUM KERNEL (ILLUSTRATIVE)
auto bell = []() __qpu__ {
cudaq::qvector q(2);
h(q[0]);
x<cudaq::ctrl>(q[0], q[1]);
mz(q);
};
THREE HYBRID WORKLOADS
1 Simulate circuits before hardware exists
2 Decode errors in real time (the µs deadline)
3 Variational loops: QPU inside a classical optimizer
Kernel syntax, device libraries, an interconnect, an ecosystem of hardware partners — item for item, this is the 2006 CUDA playbook, run again on purpose.
Notes: Facts web-verified 2026-07-16: NVQLink 400 Gb/s / <4 microseconds / 40 PF FP4; 17 QPU builders + 5 control-system providers; supercomputing-center adoption Nov 2025; cudaq-realtime public at GTC 2026; qLDPC real-time decode with Quantinuum Helios. Sources: nvidia.com/nvqlink, NVIDIA newsroom, HPCwire Jan 2026, Quantum Computing Report, Quantinuum blog. Kernel snippet is standard CUDA-Q style (illustrative). The 2^n amplitudes line is the exponential wall - why simulation alone is not enough and real QPUs are wanted at all.

## Slide 33
LOOKING FORWARD · THE NEXT SWING
Quantum pays the same bill
THE HARSHEST VERSION OF LESSON 4
To compute on data, a QPU must first LOAD it: preparing an N-value quantum state generally costs O(N) operations — unless the data has structure you can exploit.
To answer, it must MEASURE: each shot yields a handful of bits. Reading out a full N-vector costs O(N) shots. The exponential state is write-once, read-barely.
The speedup lives between those walls: computation can grow exponentially inside; the doors in and out stay narrow.
THE FLAGSHIP EXAMPLE — AND ITS FINE PRINT
HHL (2009): a quantum algorithm that “solves” a linear system in ~log N time. Note what the flagship quantum algorithm is: LINEAR ALGEBRA. The undercarriage claim, colonized by quantum computing.
The fine print: the win survives only if the matrix is sparse and well-conditioned, the input state is cheap to prepare, and you ask for a SUMMARY of the solution — an expectation value — never the whole vector x.
Demand all of x back, and the exponential advantage evaporates in the readout.
“Bring home conclusions, not matrices” turns out to be a law, not a tip: the QPU pays for its trip exactly when the computation’s growth outruns the I/O it must buy. That is the entire design question of quantum acceleration.
Notes: The user's framing made precise: quantum computation increases compute speed exponentially, but transfer (state preparation in, measurement out) does not speed up - so the advantage exists only where compute growth pays for the I/O. HHL = Harrow-Hassidim-Lloyd 2009; the caveats are the standard ones articulated in Aaronson's 'Read the Fine Print' (Nature Physics, 2015) - sparse, well-conditioned, cheap state prep, summary readout. Callback: this is the copy-back slide's decision tree at quantum scale, and one more piece of evidence for the linear-algebra thesis - even the quantum flagship is a linear solver.

## Slide 34
LOOKING FORWARD · THE NEXT SWING
The pendulum, caught mid-swing
READ IT WITH THIS DOCUMENT’S EYES
The heterogeneous machine grows another unit — the most special-purpose one imaginable, joined across a link instead of a die.
Lesson 4, made existential: qubits decohere on a deadline, so error decoding must round-trip in microseconds. The bus stopped being a tax and became life support — that is why NVQLink leads with latency, not bandwidth.
Quantum mechanics is linear in the state — the undercarriage’s last customer. Simulation is matrix arithmetic; the matmul engine was always going to be the classical half.
The runway, built on purpose this time — and either way the classical half is theirs: QEC needs their GPUs if quantum works; simulation runs on them if it stalls.
N
THE UNDERCARRIAGE · THE RUNWAY AND THE PLANE
RUN THE FREEZE CHECKLIST ON THE QPU
DOMINANT?
Not yet — no workload owns it; the killer application is still a forecast.
STABLE?
No — qubit modalities, error-correction codes, even the gate sets are still in motion.
FEEDABLE?
The open question — the <4 µs link IS the feedability problem, engineered head-on.
Three noes — which is exactly why the QPU sits across a link and not on the die. The document’s own checklist predicts the architecture.
Same pendulum, new swing — and now you know how to read it: dominant, stable, feedable. Keep the checklist.
Notes: The closer. The checklist card is the payoff of the whole seminar: the document's freeze conditions, run live on the newest hardware question, predict why the QPU is link-attached rather than on-die. Honest caution to say aloud: this is partly ecosystem positioning - today's QPUs are early-error-correction devices, and 'quantum-accelerated supercomputing' is a frame NVIDIA benefits from regardless of quantum's timeline. That is the expertResistance lesson pointed at the enthusiasts for once: test their claims too.